## Slide 1
Camera handling
Introduction to Factory IO

## Slide 2: Content
Introduction
Handling the Camera
  Orbit view
  Fly view
  First-person view

## Slide 3: Introduction
In order to properly work within your virtual factory, you will need to utilize all three different camera perspectives
Orbit view is used best in situations when you arrange objects and hence designing your factory scene
Fly view is used best in order to move around freely
First person view is used best in order to walk around in your designed factory and get an impression of whether everything fits together well and how things would be like if your factory was real.
You can change the active view by clicking one of these buttons in the upper right corner of the interface:
Orbit
First person
Fly

## Slide 4: Camera: Orbit view
Orbit view is built around a certain point of interest (“PoI”).
You can set this point either by pressing and holding the mouse wheel or by double-clicking somewhere in your scene. If using the mouse wheel, the PoI is visualized using a white dot.
You can rotate the camera freely around the PoI by clicking and holding the right mouse button and then moving the mouse. Be careful not to get dizzy as the camera won’t collide with objects or even the floor.
You can also zoom in and out by scrolling the mouse wheel.
Reset the camera to default by hitting backspace.

## Slide 5: Camera: Fly view
Fly view does not use a Point of Interest whatsoever. It is used to move around freely within the factory scene.
The easiest way to move around is to use WASD-controls or the arrow keys. The easiest way to look around is by clicking and holding the right mouse button. (The camera will rotate around itself.) In fly mode, the camera won’t move through machines etc.
You can also use the mouse wheel in order to change the height of the camera. You can also double click somewhere in order to look in that direction.
Another convenient way for moving around is to click and hold the left and right mouse button simultaneously. Move the mouse in order to change the direction of you flight.

## Slide 6: Camera: First person view
First person view is used in order to simulate a regular person within your factory. As soon as you start using this mode, camera will be brought to the ground.
Move around using WASD-controls. You can also jump up, using space!
As in fly mode, you can also move around by pressing and holding both mouse buttons simultaneously. But note that you cannot leave the ground in this move.
As in fly mode, you can change the direction of the camera by clicking and holding the right mouse button or by double clicking somewhere. (Camera will then look towards the clicked point.)

## Slide 7: Further reading
If you need further help or want to dive deeper into Factory IO, please relate to the official documentation: https://docs.factory.io
This part of the introduction is based upon part 1 (“Navigating”) of the “Getting started” section.

## Slide 8: Contact
Ing. Maarten Luyts BSc
Ing. Geert Vanhulle BSc - MBA
Ing. Dirk Van Merode MSc
AP University of Applied Sciences and Arts
maarten.luyts@ap.be
dirk.vanmerode@ap.be
Florian Eichel
FH Dortmund
sascha.pampus@fh-dortmund.de
N.K Kumar
Jimma University
rajeshtripathi63@gmail.com
Mr. Adhena Nigus
Mekelle University
nigusadhena11@gmail.com
Ms. Salama Asikuru
Muni University
s.asikuru@muni.ac.ug
8